## Slide 1: Allegro Hand Grasping System Overview
System Architecture · Modeling · Control Design · Grasp Stability

## Slide 2: System Architecture
Modular MuJoCo simulation with Allegro Hand and target object
Scene file: scene_right.xml integrates ground, table, object
Hand model: allegro_right.xml includes full joint hierarchy
Python PID controller drives grasp and lift behavior
Soft contact model for fingers; rigid or soft object geometry

## Slide 3: Modeling Details: Scene Setup
Object defined as capsule or box (e.g., cylinder_object)
Placed on table or floating in air (adjusted via XML <body> pos)
Contact parameters include friction, solimp, solref
Scene includes <equality> constraints and visual elements

## Slide 4: Modeling Details: Allegro Hand
Right hand with 16 actuated DoFs: 4 joints per finger
Base joints rootx, rooty, rootz provide translation
Each finger includes fingertip geom for contact detection
Customizable default parameters via <default> blocks

## Slide 5: Controller Design
Two-phase control: (1) descend to grasp (2) lift vertically
PID controller in Cartesian space for each fingertip
Jacobian-based projection to joint-space torque commands
Grasp condition triggers when all fingertip errors < ε

## Slide 6: Controller Justification & Tuning
Palm PID gains: Kp=0.2, Ki=0.001, Kd=0.01 (smooth approach)
Finger PID gains: Kp=1.
Differentiated thumb PID to reflect geometry difference
Lift phase uses only z-axis PID, x/y locked via feedback loop

## Slide 7: Grasp Stability: Physical Considerations
Contact parameters (friction, solref, solimp) crucial to grasping
Soft finger model allows for partial compliance and force distribution
Fingertip Jacobian ensures directional control of force application
High friction → risk of premature pushing if fingers not synchronized

## Slide 8: Grasp Stability: Control Strategies
Sequential finger control improves stability (thumb last)
Limit joint torques via np.clip to prevent overshoot
Optional lift-phase x/y locking avoids object tipping
Grasp confirmed by all fingertips within target threshold